## Slide 1: IP Adress

## Slide 2: What is an IP Address?
· Definition: Internet Protocol Address
· Function: Identifies devices on a network
· Analogy: Like a phone number for electronic devices

## Slide 3: Importance of IP Addresses
· Device-to-device communication
· Proper data routing
· Efficient network management

## Slide 4: Types of IP Addresses
IPv4:
· Length: 32 bits (4 octets)
· Format: xxx.xxx.xxx.xxx
· Example: 192.168.1.1
· Capacity: ~4.3 billion addresses
IPv6:
· Length: 128 bits
· Format: xxxx:xxxx:xxxx:xxxx:xxxx:xxxx:xxxx:xxxx
· Example: 2001:0db8:85a3:0000:0000:8a2e:0370:7334
· Capacity: 3.4×10³⁸ addresses

## Slide 5: Public vs Private Addresses
Public Addresses:
· Used on the public internet
· Allocated by organizations like IANA
· Must be globally unique
Private Addresses:
· For internal use
· Three well-known ranges
· Can be reused

## Slide 6: IPv4 Address Classes
Traditional Classful System
Class Range Networks Hosts Typical Use
A 0-127 126 16 million Large corporations
B 128-191 16,384 65,534 Universities
C 192-223 2 million 254 Small networks
D 224-239 - - Multicast
E 240-255 - - Experimental

## Slide 7: Modern Classless System (CIDR)
· Notation: Address/Network prefix
· Example: 192.168.1.0/24
· Advantages: More flexibility, reduced waste

## Slide 8: pecial Reserved Addresse
· 127.0.0.1: Localhost
· 169.254.x.x: APIPA
· 0.0.0.0: Default address

## Slide 9: IP Address Allocation

## Slide 10: Static Assignment:
Manual configuration
· Permanent address
· For servers and critical devices

## Slide 11: Dynamic Assignment (DHCP):
· Automatic from DHCP server
· Temporary lease
· For regular devices

## Slide 12: Subnetting
· Example: 255.255.255.0
· Function: Separates network portion from host portion
· CIDR notation: /24

## Slide 13: Benefits of Subnetting
· Improved performance
· Enhanced security
· Better organization

## Slide 14: Important Commands
# Windows
ipconfig
ping [address]
# Linux/Mac
ifconfig
ip addr show
ping [address]